## Slide 1
1 / 13
QUBIT 2026 HACKATHON · CHALLENGE: ANTENNA TILT
Tilting 6 Tel Aviv antennas
with a 12-qubit QAOA
Real OpenCelliD data → cost Hamiltonian → Classiq circuit → Wolfram exact simulation → Lean 4 proof
Team Quantum Headache
5-minute demo · September 2026
Notes: 0:00–0:20. One sentence: we optimise the down-tilt of 6 real Tel Aviv sector antennas with QAOA, ran it on Classiq, and verified every number two independent ways. Everything shown is reproducible from the group folder.

## Slide 2
2 / 13
SLIDE 2 / 13 | PROBLEM
The problem: pick one down-tilt per antenna
Quantum Headache · QUBIT 2026 · Antenna Tilt
Two real 3-sector sites from OpenCelliD (Ayalon, Tel Aviv). Left: all tilts 0. Right: optimum plan — only A1 tilts to level 3.
6 sector antennas A0…A5, 4 tilt levels each → 4⁶ = 4096 plans
Tilting down: less interference on neighbours, less coverage
Cost(t) = tᵀ I t − 1.5 · c·t + 0.3 · Σt (interference − coverage + penalty)
Classical brute force: unique optimum −2.844 at (0,3,0,0,0,0)
Real networks: 100s of antennas × 10 levels → intractable → quantum
Notes: 0:20–1:00. Data: opencellid_il2.csv, two 3-sector sites, interference matrix from geometry. 4096 plans is small on purpose: it lets us check the quantum answer exactly. The real operator problem (hundreds of antennas, 10 levels) has no exact classical check — that is where QAOA is meant to go.

## Slide 3
3 / 13
SLIDE 3 / 13 | MODEL
Encoding: 2 qubits per antenna, 12 qubits total
Quantum Headache · QUBIT 2026 · Antenna Tilt
tiltᵢ = q₂ᵢ + 2·q₂ᵢ₊₁ ∈ {0,1,2,3}
qᵢ = (1 − Zᵢ)/2 → Cost becomes a Pauli-Z polynomial
H_C = c₀·I + Σ hᵢ Zᵢ + Σ Jᵢⱼ ZᵢZⱼ
73 terms: 1 identity + 12 Z + 60 ZZ — strictly 2-local, no ZZZ
12
qubits
73
Pauli terms
2-local
ZZ max weight
Why binary (2 qubits) and not one-hot (4 qubits) or a dense 5-qubit pack?
Binary keeps H_C quadratic → only RZ and CX gates after ZZ decomposition
Fits Classiq student edition comfortably; 15 parallel jobs used for sweeps
QAOA layer: phase exp(+iγ H_C) then mixer RX(2β) on every qubit
Verified by Walsh–Hadamard: Pauli table reproduces all 4096 costs exactly
Notes: 1:00–1:40. Each antenna is a 2-bit number. Substituting q=(1−Z)/2 into the quadratic cost gives a Hamiltonian with only Z and ZZ terms — 73 in total, computed by gates/pauli_decomposition.py and checked against the full cost table. 2-local means the phase layer is 72 RZ rotations and CX ladders; no expensive multi-controlled gates.

## Slide 4
4 / 13
SLIDE 4 / 13 | GATES
The circuit Classiq synthesised
Quantum Headache · QUBIT 2026 · Antenna Tilt
59
depth, p = 1
114
depth, p = 2
92 CX
+ 72 RZ + 12 H + 12 RX
184 CX
+ 144 RZ + 12 H + 24 RX
Written in Qmod: QStruct of QArray[QNum[2], 6], phase(cost, γ), RX mixer
Exported as OpenQASM 3 (group/classiq/results/*.qasm) + hand-written QASM 2 layer
Same circuit re-simulated in Qiskit statevector: ⟨C⟩ = 1.9985 — identical to Wolfram
Notes: 1:40–2:10. The Qmod program uses Classiq's phase() on a QNum arithmetic expression, so the compiler builds the ZZ ladder for us. Transpiled: 12 qubits, depth 59 for one layer. We exported QASM3 and cross-checked a hand-written QASM2 of the same layer with Qiskit — three engines, same expectation value.

## Slide 5
5 / 13
SLIDE 5 / 13 | SIMULATION
Wolfram exact simulation: where the good angles are
Quantum Headache · QUBIT 2026 · Antenna Tilt
⟨C⟩(γ, β) for p = 1 over all 4096 amplitudes (statevector, no shot noise).
(0.0654, 1.1293)
optimal (γ, β), p = 1
⟨C⟩ = 1.9985
p = 1 (random: 35.5)
⟨C⟩ = −0.3825
p = 2, 4 angles
−2.844
ground state = classical optimum
Notebook + PDF + CDF + Markdown in group/wolfram/ (14 pages, 13 figures)
Landscape is flat almost everywhere — a bad start sits on a plateau at ⟨C⟩ ≈ 35
Angles found here are the warm start we hand to Classiq
Also in the notebook: VQE (RY+CZ), Grover on a 2-antenna slice, 10-level scaling
Notes: 2:10–2:50. Wolfram lets us do the full 4096-dimensional statevector and scan the whole (γ,β) plane. The optimum is a narrow valley; most of the plane is a plateau — that will matter on Classiq. These optimal angles are exported to JSON and used as warm start in the Classiq run.

## Slide 6
6 / 13
SLIDE 6 / 13 | RESULT
What the quantum sampler buys us
Quantum Headache · QUBIT 2026 · Antenna Tilt
Shots needed for 95% chance of sampling the exact optimum (Wolfram).
2.4% → 67%
P(cost < 0), random → p = 2
12270 → 342
shots to hit optimum (95%)
Half of all samples at p = 1 and two-thirds at p = 2 are already better than the baseline
Only 1–2 QAOA layers; more layers or larger p continue to sharpen the distribution
Notes: 2:50–3:20. The headline: a random plan is better than baseline 2.4% of the time; after one QAOA layer 53%; after two, 67%. The expected number of shots to see the exact optimum drops from over 12 000 to about 340. That is the gain, measured on the exact statevector and reproduced in shots on Classiq.

## Slide 7
7 / 13
SLIDE 7 / 13 | CLASSIQ
Same numbers from the Classiq simulator
Quantum Headache · QUBIT 2026 · Antenna Tilt
2.0203 vs 1.9985
⟨C⟩ p = 1, 4096 shots vs exact
0.529 vs 0.530
P(cost < 0), p = 1
Best sampled bitstring in every run = the classical optimum (0,3,0,0,0,0)
p = 2: ⟨C⟩ = −0.466 sampled vs −0.383 exact, P(cost<0) = 0.668 vs 0.67
Results, QASM and per-iteration traces saved in group/classiq/results/
Demo video: group/video/qaoa_distribution.mp4 (distribution sharpening as angles ramp)
Notes: 3:20–3:50. Switch to the live Classiq IDE / recorded screen here. Show the synthesised circuit and the histogram. The sampled expectation on the Classiq simulator agrees with Wolfram within shot noise and the most frequent low-cost sample is exactly the optimum.

## Slide 8
8 / 13
SLIDE 8 / 13 | VIDEO
Demo: the QAOA distribution sharpening
Quantum Headache · QUBIT 2026 · Antenna Tilt
120 frames, angles ramp from 0 to the p = 2 optimum
Scatter: probability of each of the 4096 plans vs its cost
Bars: P(cost < 0) climbing to 0.67
Black line: classical optimum −2.844
Second clip: group/video/classiq_convergence.mp4 — COBYLA on Classiq, iteration by iteration
Notes: 3:50–4:10. Play the clip (about 5 s). If the video does not play in the imported Canva/Google Slides deck, use the MP4 directly from the group folder.

## Slide 9
9 / 13
SLIDE 9 / 13 | CLASSIQ
Optimising on Classiq: warm start beats blind search
Quantum Headache · QUBIT 2026 · Antenna Tilt
Click to play: 20 COBYLA iterations on the Classiq simulator, one 4096-shot job each (11 s).
Start (0.20, 0.50): COBYLA stuck at ⟨C⟩ ≈ 35.5 — the plateau Wolfram predicted
Start (0.02, 0.60): 20 Classiq jobs, ⟨C⟩ 21.6 → 7.0, still above warm start 2.0
Shot noise (4096 shots) hides gradients; 15 parallel jobs let us sweep starts instead
Takeaway: exact classical pre-simulation of small instances gives angles that transfer
Notes: 4:10–4:30. Optimising angles on the sampler alone is hard: a random start sits on the plateau and COBYLA cannot see a gradient through shot noise. Warm-starting from the Wolfram angles gives the best result immediately. That is our practical recipe.

## Slide 10
10 / 13
SLIDE 10 / 13 | PROOF
Lean 4 certificates: the classical facts are machine-checked
Quantum Headache · QUBIT 2026 · Antenna Tilt
theorem decodeTilt_bijective : Function.Bijective (fun q : Fin 2 × Fin 2 => decodeTilt q.1 q.2) -- 2 qubits ↔ 4 tilts
theorem costS_optTilt : costS optTilt = -28440 -- cost ×10⁴ (decide)
theorem costS_lower_bound : ∀ t : Fin 6 → Fin 4, -28440 ≤ costS t -- 4096 cases (native_decide)
theorem costS_unique : ∀ t : Fin 6 → Fin 4, costS t = -28440 → t = optTilt -- optimum is unique
theorem cost_phase_preserves_probability : ∀ γ c a, ‖exp(γ c i) · a‖² = ‖a‖² -- phase layer keeps P
theorem two_smul_P0 / two_smul_P1 : 2•P0 = 1 + Z, 2•P1 = 1 − Z -- qubit → Pauli-Z
0 sorry
lake build succeeded
Mathlib
Lean 4.33.1
group/lean/TiltQAOA.lean + build log
Proves the optimum, its uniqueness and the encoding are exactly what the quantum runs report
Quantum layer: unitarity of the phase operator, so QAOA never destroys probability mass
Notes: 4:30–4:40. Judges asked for trust: the classical optimum, its uniqueness and the bit encoding are theorems in Lean 4 with Mathlib, checked by kernel decision procedures over all 4096 cases. No sorry.

## Slide 11
11 / 13
SLIDE 11 / 13 | SCALE
From 4 tilt levels to the operator's 10 — and beyond
Quantum Headache · QUBIT 2026 · Antenna Tilt
10 levels → 4 qubits per antenna → 24 qubits for the same 6 antennas
Hamiltonian stays 2-local: gate count grows quadratically, not exponentially
100 antennas × 10 levels ≈ 400 qubits — QAOA depth stays p·O(n²)
Grover alternative: quadratic speed-up, needs a fault-tolerant machine and an oracle for “cost < threshold”; shown on a 16-state slice in the notebook
Next: run p = 1 on IonQ simulator backend via Classiq, then hardware
Notes: 4:40–4:47. Scaling story: binary encoding grows with log of the level count; the Hamiltonian stays quadratic so the circuit stays shallow. Grover is the long-term alternative but needs error correction.

## Slide 12
12 / 13
SLIDE 12 / 13 | ARCHITECTURE
Whole network: coarse-to-fine k-means, one QAOA job per group
Quantum Headache · QUBIT 2026 · Antenna Tilt
Whole network — feature vector x_r per region
k-means, k = 5
G1
G2
G3
G4
G5
each group: joint QAOA of its antennas · 2 qubits/antenna · 2-local H_C · one Classiq job (15 in parallel)
refine G1 where ΔU is still large
G11
G12
G13
G14
G15
our run = one leaf: 2 real sites, 6 sectors, 12 qubits, optimum −2.844 found and proven
5 → 25 → 125 groups: distinct plans grow, jobs per level ≤ 25 → two batches of 15
Two stated assumptions
1. Regions in one group are similar enough to share the coarse tilt plan — refinement relaxes this level by level.
2. Interference between groups is ignored at each level — fixed by re-optimising boundary antennas with neighbours held fixed.
Group = antennas optimised jointly (the coupled ZZ problem) — that is where QAOA does work; a single shared 27-way choice would be brute-forced classically
Quantum budget per job stays what we ran today: 12 qubits = 6 antennas; 24 qubits = 6 antennas × 10 tilt levels
Classical: k-means + utility aggregation; quantum: one warm-started QAOA per group
Notes: 4:47–4:55. Whole-network story: cluster regions by a classical feature vector, k=5; each group is one QAOA job optimising its antennas jointly, 2 qubits per antenna; refine only where utility still improves. Our 12-qubit real-data run is one leaf. Two assumptions stated: shared plan within a group, no cross-group interference at a level.

## Slide 13
13 / 13
SLIDE 13 / 13 | SUMMARY
Everything is in the group folder — reproducible end to end
Quantum Headache · QUBIT 2026 · Antenna Tilt
Artifact | Path (C:\Projects\Hackton\group\…) | Key number
Classiq QAOA program + results | classiq\qaoa_tilt_classiq.py, classiq\results\*.json/*.qasm | ⟨C⟩ 2.020 (p1), −0.466 (p2)
Pauli decomposition + QASM layer | gates\pauli_terms.json, gates\qaoa_layer_schedule.qasm | 73 terms, 2-local
Wolfram notebook, PDF, CDF, MD | wolfram\wolfram_realdataset_algorithms.* | P(cost<0) 0.024→0.53→0.67
Lean 4 proof + build log | lean\TiltQAOA.lean | optimum −2.844 unique, 0 sorry
Charts + demo videos | charts\*.png, video\*.mp4 | 120 + 22 frames
Hamiltonian write-up | qaoa_antenna_hamiltonian_explanation.md | —
Team Quantum Headache — thank you. Questions?
Notes: 4:55–5:00. Close: everything is reproducible from the group folder with wolframscript, python and lake. Thank you.